## Slide 1
INFINITE ROBOTICS · FLL 2026 BIOGLOW
How to code with infinity-2026
Pull the latest code, organize runs, and make the robot do two things at once
Presented by Ethan & Braxton
Notes: Title slide. Ethan and Braxton: add today's date and the team meeting name if you like.

## Slide 2
What you will be able to do
Ethan & Braxton
1. Get the latest code
VS Code, with or without local changes
Presenter: Ethan
2. Organize and name runs
One file per run, clear names, gear setup per run
Presenter: Braxton
3. Add runs to robot.py
Pick any run by number on the hub
Presenter: Braxton
4. Multitask
Drive + attachment, color sensor, drive until line
Presenter: Ethan
5. Stop and restart a run
Center button stops, pick a new run
Presenter: Ethan
6. Practice together
A challenge to try after the talk
Presenter: Both
Notes: Who presents what is a suggestion: Ethan takes Git + multitasking + stop button, Braxton takes organizing/naming/robot.py. Swap if you prefer.

## Slide 3
Tour of the repo
Braxton
robot.py | Competition program: registers runs and starts the hub menu
ui.py | Hub menu: left/right pick a run, center starts it
robot_config.py | Wheel size, axle track, ports, attachments
robot_profiles.py | One profile per hub (ports and directions)
library.py | Shared helpers (set_drivebase)
TestRun.py | Drive one wheel rotation to test the connection
depreciated/ | Old code and demo_1 to demo_6 tutorials
✎ Braxton, fill this in: Which files will you edit most often? Where should a brand-new run file live? (Hint: repo root, not a subfolder, because the hub only uploads modules from the same folder.)
Notes: Source: README.md 'Code structure'. Note that old runs are in code_2025_unearthed/ and depreciated/.

## Slide 4
Get the latest code: no local changes
Ethan
1
Open Source Control
Click the branch icon on the left bar, or press Ctrl+Shift+G (Cmd+Shift+G on Mac).
2
Check it is clean
The Changes list is empty. If a file is listed, use the next slide instead.
3
Pull
Click the ⋯ menu, then Pull. Or click Sync Changes (↓) if it is shown.
4
Confirm
Bottom-left shows branch main with ↓0 ↑0. Open the new files in Explorer.
✎ Ethan, fill this in: Add a screenshot of each step. What does the bottom-left status bar look like before and after pull?
Notes: Terminal equivalent: git pull. Source: docs/SETUP.md section 6.

## Slide 5
Get the latest code: you have local changes
Ethan
Path A: keep my work (commit first)
1. Source Control: type a message
2. Click Commit (check only your files)
3. ⋯ menu → Pull
4. If a conflict appears, click the file and use Merge Editor: Accept Current, Incoming, or Both
Path B: set aside (stash)
1. ⋯ menu → Stash → Stash
2. ⋯ menu → Pull
3. ⋯ menu → Stash → Pop Stash
4. Fix any conflict the same way as Path A
Never commit .vscode/launch.json (it holds your own hub name). Unstage it or use Stash.
✎ Ethan, fill this in: Which path do you use, and when? What do you do when Pull says there is a conflict?
Notes: Stash = temporarily shelve changes. robot_profiles.py currently shows as modified in the repo; use this as the live demo example.

## Slide 6
Daily workflow: pull, branch, push
Ethan
1
Pull
⋯ → Pull
2
New branch
branch name (bottom-left) → Create new branch
3
Edit + test
F5 on your run file
4
Commit
message + Commit
5
Push
Publish Branch / Sync
6
Pull Request
GitHub: merge into main
✎ Ethan, fill this in: Why do we work on a branch instead of main? Who reviews the Pull Request, and who clicks Merge?
Notes: From docs/SETUP.md: pull → branch → commit → push → pull request.

## Slide 7
Organize the code for each run
Braxton
One file per run, one run function inside
Small functions for each attachment move
Driving path reads like a story, top to bottom
Runs on its own: open the file, press F5
from pybricks.tools import run_task
from robot_config import DRIVE_BASE, LEFT_ATTACHMENT
async def lift_arm_up():
await LEFT_ATTACHMENT.run_angle(720, -90)
async def run3():
await DRIVE_BASE.straight(300)
await lift_arm_up()
await DRIVE_BASE.turn(-45)
await DRIVE_BASE.straight(-300)
if __name__ == "__main__":
run_task(run3())
✎ Braxton, fill this in: Show one of your real runs. Which part is the attachment function and which part is the driving path? Where do you keep distances and angles so they are easy to tune?
Notes: README 'Writing a new run': copy run1.py, rename function, one function per attachment movement, test with F5, then add to robot.py.

## Slide 8
Name runs so anyone can find them
Braxton
Thing | Good | Avoid
Run file | run3_drone_survey.py | RogerRun.py, new2.py
Run function | async def run3() | async def go()
Attachment move | lift_arm_up() | thing1()
Constants | TO_DRONE_MM = 630 | 630 (magic number)
Note: the repo today has RogerRun.py and M1_DroneSurvey.py. Decide whether to rename them to this pattern.
✎ Braxton, fill this in: Agree on our rule: file name = run<number>_<short_mission_name>.py? Who owns each number? Write 3 naming rules the whole team will follow.
Notes: Proposed convention only. If the module is run3_drone_survey, the import is: from run3_drone_survey import run3. Keep modules in repo root.

## Slide 9
Add every run to robot.py
Braxton
from pybricks.parameters import Color
from run1_xxx import run1
from run2_xxx import run2
from run3_drone_survey import run3
# inside main(), after set_drivebase():
await add_program(run1, '1', Color.GREEN)
await add_program(run2, '2', Color.BLUE)
await add_program(run3, '3', Color.WHITE)
await user_interface() # keep this last
Menu order = order of add_program
Hub shows the number; light matches the attachment color
LEFT / RIGHT button: pick run
CENTER button: start it
✎ Braxton, fill this in: What color is each attachment set? Fill in: Run 1 = ___, Run 2 = ___, Run 3 = ___. What happens if you forget the import or the await?
Notes: robot.py currently has the add_program line commented out as an example. Source: README 'Writing a new run' step 5.

## Slide 10
Reconfigure the gear chain for each run
Braxton
from pybricks.parameters import Direction
async def run3():
# first line of the run: tell the motor what is attached
LEFT_ATTACHMENT.reconfigure(Direction.CLOCKWISE, [12, 36])
await LEFT_ATTACHMENT.run_angle(720, -90) # OUTPUT gear degrees
async def run4(): # different attachment, different gears
LEFT_ATTACHMENT.reconfigure(
Direction.COUNTERCLOCKWISE, [8, (24, 8), 40])
await LEFT_ATTACHMENT.run_angle(360, 180)
Gears list: motor gear first, final gear last
Idler gears cancel out: [8, 16, 24] = ratio 3
(24, 8) = two gears on the SAME axle
[8, 24, 8, 40] means four gears in a line
run_angle uses output angle and speed; it resets the angle each call
✎ Braxton, fill this in: Fill in per run: Run 1 gears ___ direction ___; Run 2 gears ___ direction ___. Does the motor reach the speed you ask for through the ratio?
Notes: Source: gear_swap_motor.py. reconfigure(positive_direction, gears) sets direction_x and gear_ratio; run_angle multiplies angle and speed by gear_ratio. Direction is compared to the direction the motor was created with in robot_profiles.py. Default is no gears (ratio 1). Speed is multiplied by the ratio, so a large ratio can ask the motor for more than it can do.

## Slide 11
Multitask 1: drive and move an attachment
Ethan
from pybricks.tools import multitask
async def run3():
await multitask(
DRIVE_BASE.straight(400), # lane 1: drive
lift_arm_up(), # lane 2: arm moves
)
# code below waits until BOTH are done
await DRIVE_BASE.turn(90)
Lane 1 drive ━━━━━━▶
Lane 2 arm ━━━▶
Next step starts when the slowest lane finishes.
✎ Ethan, fill this in: Run the demo (depreciated/run_demo_6_multi_tasking.py). What changed on the robot? Why does it save time on the mat?
Notes: Source: depreciated/run_demo_6_multi_tasking.py uses multitask(demo_drive_straight_turn(), demo_center_attachment()).

## Slide 12
Multitask 2: drive while the sensor watches
Ethan
async def wait_for_black(sensor, limit=15):
while await sensor.reflection() > limit:
await wait(10)
async def drive_to_line():
await multitask(
DRIVE_BASE.straight(600),
wait_for_black(RIGHT_COLOR_SENSOR),
race=True, # stop when the FIRST lane ends
)
DRIVE_BASE.stop()
# arm moves while we drive to the line
await multitask(drive_to_line(), lift_arm_up())
race=True: first lane to finish cancels the rest
Line = a known spot, so drift is reset
After the line, drive a fixed distance
✎ Ethan, fill this in: Which mission line will the sensor use to correct the position? Verify on the robot that stop() is called with or without await.
Notes: Check the exact stop call against the pybricks version on our hubs; test on the robot before the talk.

## Slide 13
Multitask 3: drive until black or white
Ethan
async def wait_for_reflection(sensor, dark, limit):
while True:
r = await sensor.reflection()
if (r < limit) if dark else (r > limit):
return
await wait(10) # check often (not 1000 ms)
async def drive_until(sensor, dark, limit, max_mm=800):
await multitask(
DRIVE_BASE.straight(max_mm),
wait_for_reflection(sensor, dark, limit),
race=True,
)
DRIVE_BASE.stop()
Measure on the mat
Black: ____
White: ____
Threshold: ____
(print reflection() and write it in)
✎ Ethan, fill this in: The color demo polls every 1000 ms. Why is that too slow for driving? Always set max_mm: what could go wrong without it?
Notes: Source: depreciated/run_demo_5_color_sensors.py shows wait_for_color polling with wait(1000); here we poll every 10 ms and use reflection() so black/white are easy to separate.

## Slide 14
Stop a run and start over
Ethan
Today
ui.py disables the built-in stop button: set_stop_button(None). Center starts a run, and nothing stops it mid-run.
Goal
Press center during a run: motors stop, the menu comes back, pick any run and start again.
# idea (Ethan's code replaces this)
async def run_with_stop(run_func):
await multitask(run_func(), wait_for_center(), race=True)
DRIVE_BASE.stop()
# stop attachments too, then return to menu
✎ Ethan, fill this in: Upload your stop-button code to the repo (branch name: ____). Paste the key lines here. How do you avoid the same center press that starts a run from stopping it right away?
Notes: Action item for Ethan: push the center-button stop code. Watch for: the center press that launches a run is still held; wait for release before listening for stop.

## Slide 15
Before you push: test checklist
Braxton
Battery charged, hub name matches launch.json
F5 on the run file: does it finish and return?
Run it three times: same result every time?
Run it from the hub menu through robot.py
Commit only your files, then open a Pull Request
If F5 fails
Use the terminal:
pybricksdev run ble --name infinite-1 TestRun.py
✎ Braxton, fill this in: Add the 2 mistakes that cost us the most time this season.

## Slide 16
Practice challenge
Ethan & Braxton
1
Pull and branch
Pull the latest code and create a branch named with your name.
2
Build a run
Copy a run file, rename it, drive to a black line while an arm moves.
3
Register and stop
Add it to robot.py as the next number, start it from the hub, stop it with center.
✎ Ethan & Braxton, fill this in: Set the deadline and who reviews the Pull Requests.

## Slide 17
Questions?
Repo: github.com/infiniteroboticsteam/infinity-2026
Setup guide: docs/SETUP.md
✎ Ethan & Braxton, fill this in: Your one-sentence takeaway for the team.